## Slide 1
PLC LADDER LOGIC DRAWING JOB 1
A Normally Open push button turns on a Red Light

## Slide 2
R
PLC PROGRAMMING JOB 1
Create this program using RSLogix 500
A Normally Open push button turns on a Red Light.

## Slide 3
PLC LADDER LOGIC DRAWING JOB 2
A Normally Open push button turns on a Red Light and a Red Light contact turns on a Green Light.

## Slide 4
G
R
PLC PROGRAMMING JOB 2
Create this program using RSLogix 500
A Normally Open push button turns on a Red Light and a Red Light contact turns on a Green Light

## Slide 5
PLC LADDER LOGIC DRAWING JOB 3
A Normally Open push button turns on a Red Light and a Red Light contact turns on a Green Light. Add a seal-in Branch circuit to hold the lights on

## Slide 6
PLC PROGRAMMING JOB 3
Create this program using RSLogix 500
A Normally Open push button turns on a Red Light and a Red Light contact turns on a Green Light. Add a seal-in Branch circuit to hold the lights on
G
R

## Slide 7
G
Y
R
G
NORMALLY OPEN
PLC PROGRAMMING JOB 4
NORMALLY CLOSED
EXAMINE IF CLOSED - XIC
EXAMINE IF CLOSED - XIC
EXAMINE IF OPEN - XIO
EXAMINE IF OPEN - XIO
Create this program using RSLogix 500

## Slide 8
PLC LADDER LOGIC DRAWING JOB 5
A Normally Open push button turns on a Red Light and a Red Light contact turns on a Green Light. Add a seal-in Branch circuit to hold the lights on. Add a Normally Closed push button to reset the circuit

## Slide 9
PLC PROGRAMMING JOB 5
Create this program using RSLogix 500
A Normally Open push button turns on a Red Light and a Red Light contact turns on a Green Light. Add a seal-in Branch circuit to hold the lights on. Add a Normally Closed push button to reset the circuit
R
G

## Slide 10
PLC LADDER LOGIC DRAWING JOB 6
A Normally Open push button turns on a Binary bit and a Binary bit contact turns on a Red Light.

## Slide 11
PLC PROGRAMMING JOB 6
Create this program using RSLogix 500
A Normally Open push button turns on a Binary bit Output and a Binary bit contact turns on a Red Light.
R

## Slide 12
PLC LADDER LOGIC DRAWING JOB 7
A Normally Open push button turns on a Binary bit Output and a Binary bit contact turns on a Green Light. Add a seal-in Branch circuit to hold the lights on.

## Slide 13
PLC PROGRAMMING JOB 7
Create this program using RSLogix 500
A Normally Open push button turns on a Binary bit Output and a Binary bit contact turns on a Green Light. Add a seal-in Branch circuit to hold the lights on.
G

## Slide 14
PLC LADDER LOGIC DRAWING JOB 8
A Normally Open push button turns on a Binary bit Output and a Binary bit contact turns on a Green Light. Add a seal-in Branch circuit to hold the lights on. Add a Normally Closed push button to reset the circuit

## Slide 15
G
PLC PROGRAMMING JOB 8
Create this program using RSLogix 500
A Normally Open push button turns on a Binary bit Output and a Binary bit contact turns on a Green Light. Add a seal-in Branch circuit to hold the lights on. Add a Normally Closed push button to reset the circuit

## Slide 16
PLC PROGRAMMING JOB 9
Create this program using RSLogix 500
(EN)
(DN)
TON
TIMER ON DELAY
TIMER T4:0
TIME BASE 0.01
PRESET 120
ACCUM 0
(EN)
(DN)
TOF
TIMER OFF DELAY
TIMER T4:1
TIME BASE 0.01
PRESET 120
ACCUM 0
(EN)
(DN)
RTO
RETENTIVE TIMER ON
TIMER T4:2
TIME BASE 0.01
PRESET 120
ACCUM 0
(RES)
(RES)

## Slide 17
PLC PROGRAMMING JOB 10
Create this program using RSLogix 500
(CU)
(DN)
CTU
COUNT UP
COUNTER C5:0
PRESET 120
ACCUM 0
(CD)
(DN)
CTD
COUNT DOWN
TIMER C5:1
PRESET 120
ACCUM 0
(RES)
(RES)

## Slide 18
We will begin building programs using word descriptions about how the program should operate. This is designed to get you to think of how to build the program on your own. You can use any of the material we have covered and as always the instructor(s) will help you if you need it. We will use programming examples each time a new item is covered

## Slide 19
PLC LADDER LOGIC DRAWING JOB 11
A Normally Open push button turns on a Binary bit Output and a Binary bit contact turns on a Green Light. Add a seal-in Branch circuit to hold the light on. Add a Binary bit contact that starts a 10 sec TIMER and when the TIMER is DONE it stops the cycle
PLC PROGRAMMING JOB 11
Create this program using RSLogix 500

## Slide 20
PLC LADDER LOGIC DRAWING JOB 12
A Normally Open push button turns on a Binary bit Output and a Binary bit contact turns on a RED Light. Add a seal-in Branch circuit to hold the light on. Add a Binary bit contact that starts a 10 sec TIMER and when the TIMER is DONE it resets the TIMER and triggers a COUNTER to count. After a count of 5 the cycle stops.
PLC PROGRAMMING JOB 12
Create this program using RSLogix 500

## Slide 21
PLC LADDER LOGIC DRAWING JOB 13
Build a 5 min clock
When a push button is pressed it starts the cycle. After the 5 min the cycle stops and a light comes on. Only use 1 timer set for 10 seconds.
PLC PROGRAMMING JOB 13
Create this program using RSLogix 500

## Slide 22
PLC LADDER LOGIC DRAWING JOB 14
Build a 5 min clock
When a push button is pressed a light comes on and starts the cycle. After the 5 min the cycle stops and a light goes off. Only use 1 timer set for 10 seconds.
PLC PROGRAMMING JOB 14
Create this program using RSLogix 500

## Slide 23
PLC LADDER LOGIC DRAWING JOB 15
PLC PROGRAMMING JOB 15
Create this program using RSLogix 500
Build a clock that will turn on all the lights in order from top to bottom
tomorrow morning at 8:30 am and stay on for 30 seconds.

## Slide 24
PLC LADDER LOGIC DRAWING JOB 16
PLC PROGRAMMING JOB 16
Create this program using RSLogix 500
When a push button is pressed, the first green light comes on 5 seconds later the red light comes, 5 seconds later the yellow light comes on and 5 seconds later the last green light comes on. Then 10 seconds after the last light comes on they go off.

## Slide 25
PLC LADDER LOGIC DRAWING JOB 17
PLC PROGRAMMING JOB 17
Create this program using RSLogix 500
When a push button is pressed, the first green light comes on 5 seconds later the red light comes, 5 seconds later the yellow light comes on and 5 seconds later the last green light comes on. Then 10 seconds after the last light comes on they start going off in the reverse order.

## Slide 26
PLC LADDER LOGIC DRAWING JOB 18
PLC PROGRAMMING JOB 18
Create this program using RSLogix 500
When a normally open push button is pressed it Moves (MOV) a constant value of 555 into integer N7:0. When the Normally Open pushbutton is pressed again it will move N7:0 into N7:1 integer. When the Normally open push button is pressed again it will Add (ADD) N7:0 and N7:1 and put that value into N7:2.

## Slide 27
PLC LADDER LOGIC DRAWING JOB 19
PLC PROGRAMMING JOB 19
Create this program using RSLogix 500
You are the owner of a parking garage. The garage has 2 levels each level holds 10 cars. You must keep track of cars entering (NO PB) and leaving (NC PB) each level. The 1st green light means the upper level can receive more cars and the 2nd green light means the lower level can receive cars. The red light means the upper level is full and the yellow light means the lower level is full. Use a selector Switch to determine which level the cars are going to enter or leave.

## Slide 28
PLC LADDER LOGIC DRAWING JOB 20
PLC PROGRAMMING JOB 20
Create this program using RSLogix 500
You own a paint mixing company. Your main tanks hold the 3 primary colors
( Red, Blue and Yellow) and each tank is controlled by a valve. A Selector switch
will determine the color we make. We are going to make 2 colors today.
The Normally Open push button will begin the filling of a barrel. The Normally
Closed push button will stop the process.
The 1st green light is the Process Running light, Red light is the Red Tank valve, Yellow light is the Yellow Tank valve and the 2nd Green light is the Blue Tank valve.
Mix Recipe
Red-Orange Dark Purple
Red 10 sec Blue 15 sec
Yellow 5 sec Red 10 sec

## Slide 29
PLC LADDER LOGIC DRAWING JOB 21
PLC PROGRAMMING JOB 21
Create this program using RSLogix 500
You work at a bottle packing facility. Your packing facility will package the product in quantities of 6, 12 or 24. First make a Start/Stop circuit using your pushbuttons. The top selector switch will distinguish between packs of 6 or 12. The bottom selector switch will be used to determine if it will be 1 pack or 2 packs to equal the amount we are looking for. For example 1 pack of 6 or 2 packs of 6 =12 or 1 pack of 12 or 2 packs of 12 = 24. The 1st green light is the process running, the red light is the pack of 6, the yellow light is a pack of 12 and the 2nd green light is a pack of 24.

## Slide 30
PLC LADDER LOGIC DRAWING JOB 22
Using what you have programmed in Job 21, add the following functionality.
A six pack takes 8 seconds to load
A twelve pack takes 13 seconds to load
Your new limit switch will indicate that a box is in place to receive bottles. Loading will start (as well as a timer). While the timer is timing, the appropriate light will blink indicating that it is filling.
When the box is full (timer is done) the light will remain solid.
Increment a counter that pertains to the type of box filled. (6,12,24 pack)
Things to consider;
Losing the box indication switch in the middle of filling.
Selector switch changing during a fill
Resetting a counter based on selector switch

## Slide 32
(EN)
(DN)
TON
TIMER ON DELAY
TIMER T4:0
TIME BASE 0.01
PRESET 120
ACCUM 0
(CD)
(DN)
CTD
COUNT DOWN
TIMER C5:1
PRESET 120
ACCUM 0
(EN)
(DN)
TON
TIMER ON DELAY
TIMER T4:0
TIME BASE 0.01
PRESET 120
ACCUM 0
(EN)
(DN)
TOF
TIMER OFF DELAY
TIMER T4:1
TIME BASE 0.01
PRESET 120
ACCUM 0
(CU)
(DN)
COUNT UP
COUNTER C5:0
PRESET 120
ACCUM 0
CTU
(EN)
(DN)
RTO
RETENTIVE TIMER ON
TIMER T4:2
TIME BASE 0.01
PRESET 120
ACCUM 0

## Slide 34
R
G
R
G
R
G

## Slide 35
R
G
https://www.plccable.com/flash-drive-allen-bradley-programming-lessons-rslogix-500-plc-training/?gclid=CIWvqJ3WjdQCFQyHaQodHCUJuw